## Slide 1
Improving Land Surface Temperature Estimates in Dust-Contaminated Atmospheres
PhD student at Faculty of Sciences of the University of Lisbon
Advisors: Sofia Ermida (IPMA), Isabel Trigo (IPMA), Carlos da Camara (IDL), & Glynn Hulley (JPL)
Francesco Stante
ESA CCI LST User Workshop, 5/6 Dec 2024

## Slide 2
Land Surface Temperature (LST)
LSA-SAF LST (clear-sky) at 2017-06-15 07:00 UTC
LST estimated using TOA brightness temperatures (BTs) of SEVIRI channels 10.8 & 12.0 µm (TIR)
Meteosat Second Generation (MSG)
Comparing LSASAF LST against ERA5 skin temperature (SKT)
LST Delta [K]: LST – SKT
seasonal means
2009 to 2012
GSW (Generalized Split-Window) algorithm
: GSW coefs. calibrated on synthetic data, varying with TCWV and VZA classes
, : average & difference of emissivities; : error
Notes: Util para avaliar a perfromance da lst,

## Slide 3
Dahra, Senegal
Niamey, Niger
LST Delta = MSG LST – ERA5 SKT [K]
Day
Night
Sahara region: 2009-2012
In situ LST comparisons
Dahra: 2009-2012
Niamey: 2006
–0.9 K / 0.1 DuAOD
CAMS EAC4 Dust Aerosol Optical Depth at 550nm (DuAOD)

## Slide 4
DuAOD-dependent GSW
GSW algorithm:
Prescribed variables from ERA5, EAC4, LSASAF:
- surface: SKT,
- atmosphere: t, q, aermr
- VZA
simulate TOA BTs using RTTOV
Calibration
calibrate GSW coefs for classes of TCWV, VZA, DuAOD using 1/3 of data
validate retrieved LST against prescribed SKT with remaining 2/3 of data
: GSW coefs. calibrated on synthetic data, varying with TCWV and VZA classes
, : average & difference of emissivities;

## Slide 5
, : average & difference of resp. emissivities
3-channel GSW:
LSASAF LST
DuAOD-dependent GSW
3-channel DuAOD-dependent GSW
Dahra station (all day)
In situ validation

## Slide 6
Uncertainties of DuAOD products
Significant errors in LST correction if DuAOD is incorrect
Potential improvement in LST is encouraging, but accurate DuAOD product required

## Slide 7
Uncertainties of DuAOD products
Impact of IFS cycle 48r1 (2023)
Adapted from CAMS June 2023 upgrade verification note
[K]
CAMS EAC4 reanalysis
before 2019
after 2019
CAMS forecast models
m = 0.0008
m = 0.002
m = 0.003
VIMaer06 [kg/m2]
VIMaer06 [kg/m2]
VIMaer06 [kg/m2]

## Slide 8
Effect of dust on MODIS LST products
LSASAF
MxD11 (GSW)
MxD21 (TES)